PUNJAB AGRO JUICES LIMITED

(A State Government Undertaking)

2 A, Sector 28-A, Chandigarh. Phone: 0172-4640060, 4639271

CIN :- U15134 CH 2006 PLC 29619

E-Mail: pajlchd@yahoo.co.in Web site: www.punjuice.in,

SHORT TERM TENDER NOTICE

PURCHASE OF GRINDING MACHINE

Punjab Agro Juices Limited, a State Government Undertaking invites sealed tenders for supply, erection & commissioning of Grinding Machine (capacity 1 T/hr & 2 T/hr) at PAJL Hoshiarpur plant on turnkey basis, suitable for grinding red/green chilies. The detailed terms and conditions can be collected from this Office/Plant or through email.

Interested parties may be submit their sealed tender alongwith earnest money for Rs.10,000/- in the shape of demand draft in favour of Punjab Agro Juices Ltd. payable at Chandigarh on or before 25.6.2015 upto 3.00 P.M. in this office.

PAJL reserves the right to accept or reject any or all tenders without assigning any reason whatsoever.

Chief Executive Officer

Terms and conditions for Supply, installation and commissioning of Grinding    Machine (capacity 1ton/hr and 2 ton / hr) on turnkey basis at PAJL Hoshiarpur.

SPECIFICATIONS

- PRODUCT: Mechanical Grinding Machine with removable SS 304 screens(0.75mm,    1.00mm, 1.5mm, 2.00mm, 2.5 mm, 3mm and 10mm )

- CAPACITY: 1 ton/hr and 2 ton / hr (separate rate should be quoted for each)

- PURPOSE: for grinding of red and green chillies

- SPECIFICATIONS: The machine structure should be fabricated from stainless steel (304 Grade). The foundation frames should be made of heavy duty MS structure with vibration control pads / grouting structure as per requirement. The machine should be provided with suitable prime mover i.e. suitable capacity Electric motor (ISI mark/ BEE approved), pulley belts, electrical and gear box etc as per requirement.

The machine should provide with all accessories, safety covers etc.

- SCOPE OF WORK: The grinding machine has to be supplied, installed and commissioned at our site on turnkey basis.

- GUARANTEE: The machine supplied should be guaranteed for a period of 12 months from the date of commissioning for any manufacturing, workmanship or any other defect.

- All inclusions/ exclusions must be clearly indicated in the tender.